HY425 – Computer Architecture
Chris Papastamos | csd4569
Assignment 1

Problem 1

Chip	#Cores	Frequency (MHz)	Memory Performance	Dhrystone Performance
Athlon 64 X2 4800+	2	2400	3423	20718
Pentium EE 840	2	2200	3228	18893
Pentium D 820	2	3000	300	15220
Athlon 64 X2 3800+	2	3200	2941	17129
Pentium 4	1	2800	2731	7621
Athlon 64 3000+	1	1800	2953	7628
Pentium 4 570	1	2800	3501	11810
Processor X	1	3000	7500	5000

i. For the normalization of each processor's benchmarks we need to use the lowest frequency CPU (Athlon 64 3000+) as a base and then calculate the rest of the normalized values (formula: NormalValue=Value/BaseValue):

Memory Performance:
Chip	Frequency (MHz)	Memory Performance	Normal Values
Athlon 64 X2 4800+	2400	3423	1.16
Pentium EE 840	2200	3228	1.09
Pentium D 820	3000	300	0.1
Athlon 64 X2 3800+	3200	2941	1
Pentium 4	2800	2731	0.92
Athlon 64 3000+	1800	2953	1
Pentium 4 570	2800	3501	1.19
Processor X	3000	7500	2.54

Dhrystone Performance:
Chip	Frequency (MHz)	Dhrystone Performance	Normal Values
Athlon 64 X2 4800+	2400	20718	2.72
Pentium EE 840	2200	18893	2.48
Pentium D 820	3000	15220	2
Athlon 64 X2 3800+	3200	17129	2.25
Pentium 4	2800	7621	1
Athlon 64 3000+	1800	7628	1
Pentium 4 570	2800	11810	1.55
Processor X	3000	5000	0.66

ii. Lets now calculate the arithmetic mean of the performance and the normalized performance
Chip	Memory Performance	Dhrystone Performance	Arithmetic Mean
Athlon 64 X2 4800+	3423	20718	12070.5
Pentium EE 840	3228	18893	11060.5
Pentium D 820	300	15220	7760
Athlon 64 X2 3800+	2941	17129	10035
Pentium 4	2731	7621	5176
Athlon 64 3000+	2953	7628	5290.5
Pentium 4 570	3501	11810	7655.5
Processor X	7500	5000	6250

Based on the above table, the processor with the highest average performance is Athlon 64 X2 4800+

For the Average Normal value of each processor we will calculate as following:

Chip	Memory Normal Value	Dhrystone Normal Value	A.M. Normal Value
Athlon 64 X2 4800+	1.16	2.72	1.94
Pentium EE 840	1.09	2.48	1.78
Pentium D 820	0.1	2	1.05
Athlon 64 X2 3800+	1	2.25	1.62
Pentium 4	0.92	1	0.96
Athlon 64 3000+	1	1	1
Pentium 4 570	1.19	1.55	1.37
Processor X	2.54	0.66	1.6

Again we can observe that the maximum average normal value is of the processor Athlon 64 X2 4800+

iii. For the Geometric Mean of the single-core and dual-core processors we will calculate based on the following formula: ratio_{gm} = nroot{2}{NormalValue_{memory}+NormalValue_{dhrystone}}

Single-Core:
Chip	Memory Normal Value	Dhrystone Normal Value	G.M. Ratio
Pentium 4	0.92	1	1.39
Athlon 64 3000+	1	1	1.41
Pentium 4 570	1.19	1.55	1.65
Processor X	2.54	0.66	1.79

Dual-Core:
Chip	Memory Normal Value	Dhrystone Normal Value	G.M. Ratio
Athlon 64 X2 4800+	1.16	2.72	1.97
Pentium EE 840	1.09	2.48	1.89
Pentium D 820	0.1	2	1.45
Athlon 64 X2 3800+	1	2.25	1.8

As we can observe the single-core processor with the greatest g.m. ratio is Processor X and the dual-core with the greatest g.m. ratio is again Athlon 64 X2 4800+

iv. For the final comparison I will compare using Weighted Arithmetic Mean. Given that 85% of the time is memory tasks and 15% is compute bound tasks, I will use weights of W_{mem}=0.85 and W_{proc}=0.15 . The formula I will use is Ratio = W_{mem}*ratio_{memory} + W_{proc}*ratio_{dhrystone}

The comparison table is as follows:
Chip	Memory Normal Value	Dhrystone Normal Value	WAM Normal Value
Athlon 64 X2 4800+	1.16	2.72	1.39
Pentium EE 840	1.09	2.48	1.3
Pentium D 820	0.1	2	0.39
Athlon 64 X2 3800+	1	2.25	1.18
Pentium 4	0.92	1	0.94
Athlon 64 3000+	1	1	1
Pentium 4 570	1.19	1.55	1.24
Processor X	2.54	0.66	2.26

We can clearly see that for the given application that 85% of the time is memory tasks and 15% is compute bound tasks, the processor with the best normal value is the Processor X.

Problem 2

i. In order to calculate the speedup of the first application when the 60% of it is parallelizable, we will do the following division:

        ParallelizationSpeedup_{1} = frac {1} {1-0.6} = 2.5

We can observe that the parallelized application will outperform the single-core application by a factor of 2.5

ii. To calculate the speedup of the second application when the 90% of it is parallelizable, we will calculate like above:

        ParallelizationSpeedup_{2} = frac {1} {1-0.9} = 10

This also means that when parallelized, the second application will achieve a speedup of 10 times

iii. If only the first application is parallelized, the overall system speedup can be calculated as follows:

        OverallSpeedup_{1} = frac {1} {(1-0.6) + frac {0.6} {2.5} } = frac {1} {0.4+0.24} = 1.56

As a result, the total system speedup will be equal to 1,56 if only the first application is parallelized

iv. In order to calculate the complete system speedup, we need to know the speedup of the second application as well:
        OverallSpeedup_{1} = frac {1} {(1-0.9) + frac {0.9} {10} } = frac {1} {0.1+0.09} = 5.26
Thus the Total System Speedup will be equal to 1,56 + 5,26 = 6,82

Problem 4
i. Based on basic calculations the MTTF of every component is the following

        MTTF_{proc}=frac {2 days} {1 processor} = 2 days/processor

        MTTF_{mem}=frac {5 days} {1 node} = 5 days/node

        MTTF_{disk}=frac {25 days} {1 disk} = 25 days/disk

ii. In order to calculate the MTTF of the system as a whole we need to consider the failure rates of all the components:

        MTTF_{system} = frac {1} {{frac {1} {MTTF_{proc}}}+{frac {1} {MTTF_{mem}}}+ {frac {1} {MTTF_{disk}}} } = frac {1} {{frac {1} {2}} + {frac 1 5} + {frac 1 25}} = frac 1 0.74 = 1.35 days

iii. In order to calculate the availability of the system we need to use the following formula:

        SystemAvailability = frac {MTTF} {MTTF + MTTR} = frac {1.35*24} {(1.35*24) +1} = frac {32.43} {33.43} = 0.97

Which leads us with a system with 97% availability