HY425 – Computer Architecture
Chris Papastamos | csd4569
Assignment 2

Problem 1
i. For the execution of one itteration of the given loop I will calculate each instruction delay as their respective delay +1 for their instruction fetch.

Instruction					Cycles
Loop:	LD	F2,	0(Rx)		1+4=5
I0:	DIVD	F8,	F2,	F0	1+8=9
I1:	MULTD	F2,	F6,	F2	1+3=4
I2:	LD	F4,	0(Ry)		1+4=5
I3:	ADDD	F4,	F0,	F4	1+2=3
I4:	ADDD	F10,	F8,	F2	1+2=3
I5:	ADDI	Rx,	Rx,	8	1+0=1
I6:	ADDI	Ry,	Ry,	8	1+0=1
I7:	SD	F4,	0(Ry)		1+1=2
I8:	SD	F2,	0(Rx)		1+1=2
I9:	SUB	R20,	R4,	Rx	1+0=1
I10:	BNZ	R20,	Loop		1+1=2
Total:					38 Cycles

ii.

Instruction					Strart Cycle	Ending Cycle
Loop:	LD	F2,	0(Rx)		1	6
I0:	DIVD	F8,	F2,	F0	7	16	<stall>
I1:	MULTD	F2,	F6,	F2	8	12
I2:	LD	F4,	0(Ry)		9	14
I3:	ADDD	F4,	F0,	F4	15	18	<stall>
I4:	ADDD	F10,	F8,	F2	17	20	<stall>
I5:	ADDI	Rx,	Rx,	8	18	21
I6:	ADDI	Ry,	Ry,	8	19	22
I7:	SD	F4,	0(Ry)		23	25	<stall>
I8:	SD	F2,	0(Rx)		24	26
I9:	SUB	R20,	R4,	Rx	25	26
I10:	BNZ	R20,	Loop		27	29	<stall>

The pipeline will run for 29 Cycles!

iii.

Instruction					Strart Cycle	Ending Cycle
Loop:	LD	F2,	0(Rx)		1	6
I0:	LD	F4,	0(Ry)		2	7
I1:	ADDI	Rx,	Rx,	8	3	6
I2:	ADDI	Ry,	Ry,	8	4	7
I3:	DIVD	F8,	F2,	F0	7	16	<stall>
I4:	ADDD	F4,	F0,	F4	8	9
I5:	MULTD	F2,	F6,	F2	9	13
I6:	SUB	R20,	R4,	Rx	10	11
I7:	SD	F4,	0(Ry)		11	13
I8:	SD	F2,	0(Rx)		12	14
I9:	ADDD	F10,	F8,	F2	16	20	<stall>
I10:	BNZ	R20,	Loop		17	18

The reordered code will run for 18 Cycles!

iv.

…

Problem 2
In left table we can see the instructions before register renaming. The colored registers need to be renamed in order to achieve maximum efficiency. In the table on the right is the loop using the renamed registers

Instruction					Instruction
Loop:	LD	F2,	0(Rx)			Loop:	LD	F2,	0(Rx)
I0:	DIVD	F8,	F2,	F0		I0:	DIVD	F8,	F2,	F0
I1:	MULTD	F2,	F6,	F2		I1:	MULTD	F2a,	F6,	F2
I2:	LD	F4,	0(Ry)			I2:	LD	F4,	0(Ry)
I3:	ADDD	F4,	F0,	F4		I3:	ADDD	F4a,	F0,	F4
I4:	ADDD	F10,	F8,	F2		I4:	ADDD	F10,	F8,	F2a
I5:	ADDI	Rx,	Rx,	8		I5:	ADDI	Rxa,	Rx,	8
I6:	ADDI	Ry,	Ry,	8		I6:	ADDI	Rya,	Ry,	8
I7:	SD	F4,	0(Ry)			I7:	SD	F4a,	0(Rya)
I8:	SD	F2,	0(Rx)			I8:	SD	F2a,	0(Rxa)
I9:	SUB	R20,	R4,	Rx		I9:	SUB	R20,	R4,	Rxa
I10:	BNZ	R20,	Loop			I10:	BNZ	R20,	Loop

The new registers used are: F2a, F4a, Rxa and Rya
ii. Lets now look at the execution of this code snippet with renamed registers:

Instruction					FU	Start Clock	Ending Clock
Loop:	LD	F2,	0(Rx)		LD/SD	1	6
I0:	DIVD	F8,	F2,	F0	ALU0	7	16
I1:	MULTD	F2a,	F6,	F2	ALU1	8	12
I2:	LD	F4,	0(Ry)		LD/SD	6	9
I3:	ADDD	F4a,	F0,	F4	ALU0	13	16
I4:	ADDD	F10,	F8,	F2a	ALU1	17	20
I5:	ADDI	Rxa,	Rx,	8	ALU0	2	3
I6:	ADDI	Rya,	Ry,	8	ALU1	3	4
I7:	SD	F4a,	0(Rya)		LD/SD	17	19
I8:	SD	F2a,	0(Rxa)		LD/SD	21	23
I9:	SUB	R20,	R4,	Rxa	ALU0	4	5
I10:	BNZ	R20,	Loop		ALU1	5	6